Run plan: Compton scatter (2019-03-13)

In order to study whether or not the Compton edge can be improved in terms of resolution, two detector can be used in logic AND and used to trigger the data acquisition of the first detector as a function of scattering angle of the gamma ray.

Material:
- Gamma source (Cs-137, Co-60 or Na-22)
- NE213 cup detector
- One gamma detector (YAP/LaBr)
- NIM crate
- Discriminator (CFD) module
- Logic AND/OR module
- Pocket MCA

Procedure:
1) Determine CFD threshold.
2) Baseline run: MCA on NE213 detector signal no logic.
3) Angle test: Include gamma detector at set angle relative NE213

Estimated time:
Setup: 1h
Test/verification/modification: 1h
Run: Self sufficient, overnight

Setup:
(I-L H. KNOX, T. G. MILLERA: “TECHNIQUE FOR DETERMINING BIAS SETTINGS FOR ORGANIC SCINTILLATORS”)