Run plan: Calibration runs (2019-03-24)

Na-22 and Cs-137 will be used to calibrate “cup” scintillators and analog DAQ QDC to MeVee. The detector will be encapsulated in lead and plastic shielding. The PuBe source will be parked and the plug will be in the beamport.
Questions:
- Can I use the DAQ as-is for source calibration?
- Are the detector signals blocked (latch) after initial trigger?
- If not, there may be unwanted signals making it through in the time between detector start and YAP stop.
- Does the DAQ need modifications?
Material:
- Gamma sources: Na-22 and Cs-137
- Aquarium and TOF DAQ (analog)
- Scintillator cups
- Shielding material (lead/plastic)

Procedure:
1) Build shielding around detector
2) Modify and test DAQ if needed
3) Force pedestal using YAP signal
4-...) Run with Na-22 and Cs-137 separately for each scintillator

Results:
- To get QDC spectrum showing Compton edges for 511, 1275 and 662 keV for each scintillator.
- Calibrate each detector to MeVee

Estimated time:
Setup: 2h
Test/verification/modification: 2h
Run: Prob 1 week for all cups (ca 24h each)